## Slide 1: Research Methodology
Research on attack scenarios
Implementation and testing of ML model
Research on ML models
Research on normal scenarios
Evaluation of ML model
Creation of Testing Dataset
Creation of Training Datasets
Initial research on smart grids and cyber threats
Integration of best ML model in IDS

## Slide 2: Training Datasets Breakdown
 | Constrained | NCombined | Unique Normal | Unique Normal Options Random
Config Violation: Trafo1 | 0 | 0 | 0 | 1294
Config Violation: Trafo2 | 0 | 0 | 0 | 1686
Config Violation: Trafo3 | 0 | 0 | 0 | 1671
Config Violation: Feeder1 | 0 | 239 | 5 | 128
Config Violation: Feeder2 | 0 | 208 | 567 | 1034
Config Violation: Feeder3 | 0 | 239 | 589 | 953
Lines over 80% | 7914 | 582 | 2016 | 2445
Load Lost > 20% | 0 | 1783 | 5442 | 1772
Transformers over 80% | 1428 | 275 | 5653 | 5624
More than 8 open switches | 3247 | 699 | 2176 | 407
bus PU violated | 0 | 0 | 140 | 170
No anomaly | 7411 | 15975 | 59953 | 28497
Total | 20000 | 20000 | 76541 | 45681

## Slide 3: Testing Datasets Breakdown
 | Unconstrained | Attack | Special
Config Violation: Trafo1 | 5002 | 65536 | 0
Config Violation: Trafo2 | 586 | 16384 | 0
Config Violation: Trafo3 | 83 | 4096 | 0
Config Violation: Feeder1 | 10112 | 131072 | 0
Config Violation: Feeder2 | 3705 | 32768 | 0
Config Violation: Feeder3 | 446 | 8192 | 0
Lines over 80% | 6 | 0 | 8361
Load Lost > 20% | 0 | 0 | 0
Transformers over 80% | 0 | 0 | 6639
More than 8 open switches | 56 | 0 | 0
bus PU violated | 1 | 0 | 0
No anomaly | 3 | 4096 | 5000
Total | 20000 | 262144 | 20000

## Slide 4: Powergrid Dataset Generation
Jia Wei

## Slide 5: Types of Datasets
Unconstrained
Constrained
Normal without Disturbance
Normal with Disturbance
NCombined (Normal without Disturbance + Normal with Disturbance)
Special
Unique Normal (4096 Unique Normal Configurations x 5 load profiles x 5 toggling options)
Attack Dataset

## Slide 6: Power Grid
Substation 1:
  Feeder Lines: L0, L4 (CB0, CB4)
  Feeder Breakers: CB-3
  Transformers: T0, T1
  Transformer Breaker: CB-10
  Lines: L0 – L16 (Less L3 and L10)
Substation 2:
  Feeder Lines: L2, L5 (CB2-CB151, CB5-CB152)
  Bus Coupler Breakers: CB-153
  Transformers: T2, T3
  Transformer Breaker: CB-158
  Lines: L14 – L21
Substation 3:
  Feeder Lines: L1, L6 (CB1-CB171, CB6-CB172)
  Bus Coupler Breakers: CB-173
  Transformers: T4, T5
  Transformer Breaker: CB-178
  Lines: L22 – L25
s
GRID
GRID
110kV
110kV
110kV
110kV
10kV
10kV
10kV
10kV
110kV
110kV
S/S-1
S/S-2
S/S-3
10kV
10kV
Line L1
Line L2
Line L5
Line L6
CB-3
CB-10
CB-153
CB-158
CB-173
CB-178
T0
T1
T2
T3
T4
T5
Line L0
Line L4
Line L7
Line L8
Line L9
Line L11
Line L12
Line L13
L14
L15
L16
L17
L18
L19
L20
L21
L22
L23
L24
L25
CB-151
CB-152
CB-171
CB-172
load0
load1
load2
load3
load4
load5
load6
load7
load8
load9
load10
load11
load12
load13
load14
load15
load16
load17
Feeder0
Feeder1
CB-0
CB-4
CB-1
CB-2
CB-5
CB-6
CB-7
CB-8
CB-9
CB-11
CB-12
CB-13
CB-14
CB-15
CB-16
CB-17
CB-18
CB-19
CB-20
CB-21
CB-22
CB-23
CB-24
CB-25
Bus_0
Bus_1
Bus_2
Bus_3
Bus_5
Bus_6
Bus_4
Bus_7
Bus_8
Bus_9
Bus 10-15
Bus_16
Bus_17
Bus 20 -27
Bus_18
Bus_19
Bus 28 - 31

## Slide 7: Summary of Training Dataset Generation
Step 1:
Use Pandapower to initialize grid layout
Set up Standard Grid layout
Create .csv and initialize headers for CBs/Loads/Trafos/Feeders
Initialize preset loads for lines 7-25
NCombined
Initialize Options and datasets factor
2. Creating different datasets by starting at a non-anomalous datapoint
2a. This non-anomalous datapoint can be of any valid configuration that ensures for each substation, at least 1 transformer and feeder is online and connected with load randomized. (See constrained)
2b.Apply options on each previous datapoint in the dataset sequentially. If anomaly found in datapoint or no more options left, restart and generate a new dataset.
3. Stop when the number of datasets created hits the desired amount
Pseudocode:
Unique_Normal
Initialize 4096 Unique Grid Configurations that are valid
2. Initialize Options + Set up different load profiles
3. Generate different datapoints for each of the 4096 unique config
3a. For each config, create X different starting points based on X load profiles
3b. For each starting point, generate Y different datapoints by applying Y options. Options are applied on the previous datapoint sequentially. If anomaly found in datapoint, stop applying options and continue to next starting point.
Pseudocode:
Constrained
Constrained:
Randomize the loads in line 7-25 ranging from 70%-130% of the preset load
This non-anomalous datapoint can be of any valid configuration that ensures for each substation, at least 1 transformer and feeder is online and connected with load randomized.
Randomly switch on/off any load switches

## Slide 8: Summary of UNOR Dataset Generation
Step 1:
Use Pandapower to initialize grid layout
Set up Standard Grid layout
Create .csv and initialize headers for CBs/Loads/Trafos/Feeders
Initialize preset loads for lines 7-25
Unique Normal Options Random
Initialize 4096 Valid Unique Grid Configurations
2. Initialize Options + Set up different load profiles
3. Generate different datapoints for each of the 4096 unique config
3a. For each config, create X different starting points based on X different load profiles
3b. For each starting point, generate Y different datapoints by applying Y options, followed by randomly switching on or off ANY switches (34CBs + 6Trafos + 2 Feeders).
3d. Options are applied on the previous datapoint sequentially. If anomaly found in datapoint, stop applying options and continue to next starting point.
3c. In total, ideally we should have 4096 * X * Y datapoints (Y can vary if anomaly found)
Pseudocode:

## Slide 9: Summary of Testing Dataset Generation
Step 1:
Use Pandapower to initialize grid layout
Set up Standard Grid layout
Create .csv and initialize headers for CBs/Loads/Trafos/Feeders
Initialize preset loads for lines 7-25
Attack
Special
Initialize Options and Error point factor and datasets factor
2. Creating different datasets by starting at a non-anomalous datapoint
2a. This non-anomalous datapoint can be of any valid configuration that ensures for each substation, at least 1 transformer and feeder is online and connected with load randomized. (See constrained)
2b. Set this datapoint as the starting datapoint
2c. Apply options on it till we get an anomalous datapoint.
2d. Repeat 2c for X number of times till we get X anomalous datapoint for 1 non-anomalous starting datappint.
3. Repeat 2,2a,2b,2c till the number of datasets created hits the desired amount.
Pseudocode:
Initialize all 8^6 Unique Grid Configurations
2. Run powerflow simulation for each of the grid configuration and save results to csv file.
Pseudocode:
Unconstrained:
Randomize the loads in line 7-25 ranging from 70%-130% of the preset load
Randomly switch on/off any switches/transformers/feeders
Unconstrained

## Slide 10: Load Profiles
Load 1 = 0-40%, Load 2=40-60%, Load 3=60-80%, Load 4=80-100%, Load 5=100-130%, Load 6=130-150%
load_profiles = [[0,40], [40,70], [70,100], [100,120], [120,150]]

## Slide 11: Options
Options: ['feeder_0', 'feeder_1', 'feeder_2', 'trafo_0', 'trafo_1', 'trafo_2', 'switch_7', 'switch_8', 'switch_9', 'switch_11', 'switch_12', 'switch_13', 'switch_14', 'switch_15', 'switch_16', 'switch_17', 'switch_18', 'switch_19', 'switch_20', 'switch_21', 'switch_22', 'switch_23', 'switch_24', 'switch_25’]
Feeder option:
  Feeder_0: External to Substation 1, Feeder_1: SS1 to SS2, Feeder_3: SS1 to SS3
  Turn off 1 random feeder (line), then enable corresponding coupler, For each turned off feeder (line), open at least 1 switch in the corresponding line

## Slide 12: Options
Options: ['feeder_0', 'feeder_1', 'feeder_2', 'trafo_0', 'trafo_1', 'trafo_2', 'switch_7', 'switch_8', 'switch_9', 'switch_11', 'switch_12', 'switch_13', 'switch_14', 'switch_15', 'switch_16', 'switch_17', 'switch_18', 'switch_19', 'switch_20', 'switch_21', 'switch_22', 'switch_23', 'switch_24', 'switch_25’]
Transformer option:
  trafo_0: Transformers in SS1, trafo_1: Transformers in SS2, trafo_2: Transformers in SS3
  Turn off 1 random transformer and enable corresponding output coupler

## Slide 13: Options
Options: ['feeder_0', 'feeder_1', 'feeder_2', 'trafo_0', 'trafo_1', 'trafo_2', 'switch_7', 'switch_8', 'switch_9', 'switch_11', 'switch_12', 'switch_13', 'switch_14', 'switch_15', 'switch_16', 'switch_17', 'switch_18', 'switch_19', 'switch_20', 'switch_21', 'switch_22', 'switch_23', 'switch_24', 'switch_25’]
Switch option:
  Switch_7 to Switch_25: All switches connecting to lines with loads to external buses (L7-25)
  For special dataset: close the switch to connect the line to the grid
  For Unique_Normal/Ncombined dataset: open the switch to disconnect the line from the grid

## Slide 14: Old Datasets

## Slide 15: High Level Dataset Generation Steps
Common to all Datasets
Step 1: Initialization of Power Grid
Use Pandapower to create the grid template as shown in previous slide
Initialise switches (CB), loads, transformers and feeder index for .csv
Initialise loads to all lines connecting to external buses (L7-L25)
  Load values preset for each lines in pandapower_net.py (Multiplied by load_mult_factor (2.8) to increase chance of anomalous datapoint incidence)

## Slide 16: High Level Dataset Generation Steps
Specific to different Datasets
Step 2: Generation of datapoints
Generate datapoints till number of datapoints == Requested amount
For each datapoint, we first randomized the load values of the lines by multiplying the preset load values with a random percentage between 70 – 130% (Load Variance)
We then call vary_grid() function, that is specific to different datasets

## Slide 17: High Level Dataset Generation Steps
Unconstrained vary_grid()
  Randomly close any feeder lines, switches, transformers with no context.
  Do this for all datapoints and run the powerflow state stimulation for each datapoint to get results.
Step 3: Add datapoint result to .csv

## Slide 18: High Level Dataset Generation Steps
Constrained/Normal with Disturbance vary_grid()
  This dataset ensures that for each substation, at least 1 transformer/feeder is online and connected.
  The feeder/transformer bus couplers will be activated if needed (except for CB-3 and CB-10 which are always closed) such that all loads are still connected in the grid unless their respective switches are open
    E.g. Line 2 from substation 1 to substation 2 is open/disconnected, CB-153 will then close to ensure the loads at L14-17 are still connected.
  All other non-constrained switches are closed/open randomly
  Constrained Switches:
    Feeder Switches: Substation 1: (0, 4), Substation 2: (2, 5, 151, 152), Substation 3: (1, 6, 171, 172)
    Coupler Switches: Substation 1: (3, 10), Substation 2: (153, 158), Substation 3: (173, 178)
  Non-constrained Switches: CB7-25
Step 3: For constrained dataset, we add datapoint result to .csv
For normal with disturbance, we do further processing before adding to the csv file. More info later.

## Slide 19: Normal with/without Disturbance and Special Dataset
The generation of these data requires special processing by making a dataset instead of a datapoint for each iteration.
For each dataset, we first generate 1 datapoint.
Normal without Disturbance datapoint: All feeder lines, transformers and switches are closed, online and connected except for the bus coupler circuit breakers (CB-153, CB158, CB173, CB178).
Normal with Disturbance datapoint: A constrained datapoint is generated. (See previous slide)
Special Datapoint: All loads are disabled first, before randomly applying X number “options” to the grid (Default is 5). We then run the powerflow simulation and ensure that this config is non-anomalous. If it is anomalous, we restart and keep repeating till the config is non-anomalous.
See next slide on how options work. It is used for normal with/without disturbance and special dataset.

## Slide 20: Options
Options: ['feeder_0', 'feeder_1', 'feeder_2', 'trafo_0', 'trafo_1', 'trafo_2', 'switch_7', 'switch_8', 'switch_9', 'switch_11', 'switch_12', 'switch_13', 'switch_14', 'switch_15', 'switch_16', 'switch_17', 'switch_18', 'switch_19', 'switch_20', 'switch_21', 'switch_22', 'switch_23', 'switch_24', 'switch_25’]
Feeder option:
  Feeder_0: External to Substation 1, Feeder_1: SS1 to SS2, Feeder_3: SS1 to SS3
  Turn off 1 random feeder (line), then enable corresponding coupler, For each turned off feeder (line), open at least 1 switch in the corresponding line

## Slide 21: Options
Options: ['feeder_0', 'feeder_1', 'feeder_2', 'trafo_0', 'trafo_1', 'trafo_2', 'switch_7', 'switch_8', 'switch_9', 'switch_11', 'switch_12', 'switch_13', 'switch_14', 'switch_15', 'switch_16', 'switch_17', 'switch_18', 'switch_19', 'switch_20', 'switch_21', 'switch_22', 'switch_23', 'switch_24', 'switch_25’]
Transformer option:
  trafo_0: Transformers in SS1, trafo_1: Transformers in SS2, trafo_2: Transformers in SS3
  Turn off 1 random transformer and enable corresponding output coupler

## Slide 22: Options
Options: ['feeder_0', 'feeder_1', 'feeder_2', 'trafo_0', 'trafo_1', 'trafo_2', 'switch_7', 'switch_8', 'switch_9', 'switch_11', 'switch_12', 'switch_13', 'switch_14', 'switch_15', 'switch_16', 'switch_17', 'switch_18', 'switch_19', 'switch_20', 'switch_21', 'switch_22', 'switch_23', 'switch_24', 'switch_25’]
Switch option:
  Switch_7 to Switch_25: All switches connecting to lines with loads to external buses (L7-25)
  For special dataset: close the switch to connect the line to the grid
  For normal with/without disturbance dataset: open the switch to disconnect the line from the grid

## Slide 23: Normal with/without Disturbance
After creation of the first datapoint, we then apply options till an anomalous result is generated OR we run out of options to play with.
For each time an option is applied, we create a new datapoint and run the powerflow simulation. We add this new datapoint to the dataset.
Hence, the dataset in the generation of Normal with/without Disturbance will firstly have 1 starting datapoint, following by multiple datapoints that is created by applying options one step at a time (Options are removed each time they are applied)
We stop till a datapoint is deemed to be an anomalous result or there are no options to apply left  This results in a dataset
Repeat the process to create X number of dataset

## Slide 24: Special
After creation of the first datapoint, we then apply one option at a time and for each option applied, we run the powerflow simulation. If it is an anomalous result, we add it to the dataset. If not, we apply another option and run again, repeating the process till we get an anomalous result.
  We then restore the state of the grid to its original first datapoint state and apply options again.
  Repeat this process till we get X number of anomalous datapoint for each starting datapoint.
  If we run out of options and the result generated is not an anomaly, we generate a new first datapoint and try again.
So for each normal datapoint generated, we need to generate X number of anomalous datapoints. This will become a dataset.
Repeat the process till we hit K number of datasets

## Slide 25: NCombined
This dataset comprises of combining the Normal with Disturbance dataset and Normal without Disturbance Dataset